## Slide 1
Predicting Performance of Integrated Circuits using Regression Analysis
DS6372: Project 1
Joanna Duran, Nikhil Gupta, Max Moro

## Slide 2: Agenda
Introduction
Motivation and Goal
Dataset and Data Collection Process
Exploratory Data Analysis
Following Good Modeling Practices
Full Model Analysis
  Issues Identified
  Avoiding temptation of removing high influence points
Model refinement with Variable Selection Techniques
  Forward Selection, Backward Elimination, Stepwise Selection
  LASSO, LARS
Conclusions and future recommendations for model improvement

## Slide 3: Introduction
Semiconductor manufacturing is a variable process and outcomes depending on several factors.
In order to meet target specifications, some parameters are controlled by engineers, however some are beyond human control (e.g. process variation).
Manufacturing process variation leads to output variables varying between a min and max value
Challenges:
  Range is typically measured after the manufacturing process is completed and all R&D has been done
  Not all values can be practically measured (due to time, resource and cost constraints)
  Can lead to issues if the variation of output is outside target specs
Reference

## Slide 4: Motivation and Goal
Can we predict the limits before the integrated circuits are manufactured to preemptively make changes when specs are expected to be out of range?
  Yes, using electrical simulation (+ running Monte Carlo simulations)
  However, this is very resource intensive as each electrical simulation can take several hours
Hence our goal is to build a model to predict the performance of the output variables. Specifically,
  Pick the most critical output variable
  Build a model to predict the mean value of the output
    Free to choose any variables of liking from the model
    Target accuracy: +/- 10% desired, but +/- 15% would be acceptable also

## Slide 5: Dataset and Collection Process
10,000 rows capturing the performance of the circuit under various conditions.
240 features
  x1 - x23: values that can be controlled by engineers to tune the performance
    Wide range of values, some ranging from to 100, others are in the Nano or Micro range
  stat1 – stat217: process variation parameters beyond human control
    Range from -3 to 3, with mean of 0
    Values represent sigma variation around mean
  Output variable to target: y3 (most critical)
Data Collection Process
  Engineer controlled variables were uniformly randomly sampled from their design space (since engineers can select any values from range)
  Statistical features were also uniformly randomly sampled since we wanted accuracy of model to be good throughout statistical variation range and not just closer to the population means.
Notes: Add histogram and density plots for 2 x variables (different ranges), and 1 stat variable

## Slide 6: Exploratory Data Analysis | Output Variable
3020 cases have NA values for output variables
  Consulted with domain expert. Not valid features in combination  Can be removed without affecting inference capability
Output Variable (y3):
  Shows right skewed histogram
  Log transformation helps a bit, hence we proceeded with taking log transformation
  Note: log base 10 is more common in this industry, hence that is used instead of natural log

## Slide 7: Exploratory Data Analysis | Features (1)
Correlation of Features to each other
  Check for multicollinearity
  Since inputs were randomly sampled, we did not expect there to be multicollinearity
  Correlation table and VIF values confirmed the same
 | x1 | x2 | x3 | x4 | x5 | x6 | x7 | x8 | x9 | x10
x1 | 1.0000 | 0.0034 | -0.0028 | 0.0085 | 0.0068 | 0.0159 | 0.0264 | -0.0012 | 0.0142 | 0.0013
x2 | 0.0034 | 1.0000 | -0.0057 | 0.0004 | -0.0094 | -0.0101 | 0.0089 | 0.0078 | 0.0049 | -0.0214
x3 | -0.0028 | -0.0057 | 1.0000 | 0.0029 | 0.0046 | 0.0006 | -0.0105 | -0.0002 | 0.0167 | -0.0137
x4 | 0.0085 | 0.0004 | 0.0029 | 1.0000 | -0.0059 | 0.0104 | 0.0098 | 0.0053 | 0.0061 | -0.0023
x5 | 0.0068 | -0.0094 | 0.0046 | -0.0059 | 1.0000 | 0.0016 | -0.0027 | 0.0081 | 0.0259 | -0.0081
x6 | 0.0159 | -0.0101 | 0.0006 | 0.0104 | 0.0016 | 1.0000 | 0.0200 | -0.0157 | 0.0117 | -0.0072
x7 | 0.0264 | 0.0089 | -0.0105 | 0.0098 | -0.0027 | 0.0200 | 1.0000 | -0.0018 | -0.0069 | -0.0221
x8 | -0.0012 | 0.0078 | -0.0002 | 0.0053 | 0.0081 | -0.0157 | -0.0018 | 1.0000 | 0.0142 | -0.0004
x9 | 0.0142 | 0.0049 | 0.0167 | 0.0061 | 0.0259 | 0.0117 | -0.0069 | 0.0142 | 1.0000 | 0.0149
x10 | 0.0013 | -0.0214 | -0.0137 | -0.0023 | -0.0081 | -0.0072 | -0.0221 | -0.0004 | 0.0149 | 1.0000
vifDF = usdm::vif(select_at(data,predictors)) %>% arrange(desc(VIF)) head(vifDF,15)
## Variables VIF ## 1 stat204 1.063870 ## 2 stat175 1.063370 ## 3 stat66 1.062060 ## 4 stat105 1.062008 ## 5 x6 1.061394 ## 6 stat2 1.061388 ## 7 stat14 1.061212 ## 8 x7 1.060532 ## 9 stat216 1.060477 ## 10 stat142 1.060190 ## 11 stat154 1.059695 ## 12 stat32 1.059608 ## 13 stat141 1.059564 ## 14 stat138 1.059507 ## 15 stat73 1.059386
Notes: Add the important scatterplots

## Slide 8: Exploratory Data Analysis | Features (2)
Correlation of Features to y3.log
  Shows that very few features are highly correlated (positive or negative) with output
  Same is visible from the scatter plots of output vs. inputs
  Hence, features by themselves may not have a lot of predictive power
variable | y3.log
x18 | 0.3120
x7 | 0.2091
stat98 | 0.1784
x9 | 0.1127
x17 | 0.0611
x16 | 0.0489
x10 | 0.0472
x21 | 0.0412
x11 | 0.0322
x8 | 0.0318
stat156 | 0.0287
stat23 | 0.0234
stat100 | 0.0206
stat144 | 0.0203
stat59 | 0.0202
stat60 | 0.0199
stat195 | 0.0199
stat141 | 0.0194
stat73 | 0.0192
stat197 | 0.0185
variable | y3.log
stat110 | -0.1594
x4 | -0.0603
stat13 | -0.0345
stat41 | -0.0345
stat14 | -0.0317
stat149 | -0.0309
stat113 | -0.0279
stat4 | -0.0248
stat106 | -0.0236
stat146 | -0.0236
stat186 | -0.0217
stat91 | -0.0210
stat214 | -0.0209
stat5 | -0.0207
stat22 | -0.0202
stat39 | -0.0202
stat175 | -0.0194
stat187 | -0.0193
stat128 | -0.0192
stat37 | -0.0191
Notes: Add the important scatterplots

## Slide 9: Exploratory Data Analysis | Features (3)
Feature Transformation
  For the most highly correlated features, x18, shows a slight curvature in the scatter plot
  Minor improvement to linearity can be obtained by using a square root transformation on x18.
Notes: Add the important scatterplots

## Slide 10: Following Good Modeling Practices
Avoiding overfitting
  Even though we have a lot of data points, with so many features it is possible to overfit the data
  Hence, we split our dataset into Train and Test splits (80:20 ratio).
During training process, 10-fold cross validation technique was used for model selection
  Allows for the use of the entire training dataset for model development
Source

## Slide 11: Full Model Analysis
Start by analyzing the full model consisting of all 240 features with appropriate transformations
Analyze fit statistics
Analyze the plots for issues with model assumption.
This will guide the next step in the process.
## y3.log ~ x1 + x2 + x3 + x4 + x5 + x6 + x7 + x8 + x9 + x10 + x11 + ## x12 + x13 + x14 + x15 + x16 + x17 + x19 + x20 + x21 + x22 + ## x23 + stat1 + stat2 + stat3 + stat4 + stat5 + stat6 + stat7 + ## stat8 + stat9 + stat10 + stat11 + stat12 + stat13 + stat14 + ## stat15 + stat16 + stat17 + stat18 + stat19 + stat20 + stat21 + ## stat22 + stat23 + stat24 + stat25 + stat26 + stat27 + stat28 + ## stat29 + stat30 + stat31 + stat32 + stat33 + stat34 + stat35 + ## stat36 + stat37 + stat38 + stat39 + stat40 + stat41 + stat42 + ## stat43 + stat44 + stat45 + stat46 + stat47 + stat48 + stat49 + ## stat50 + stat51 + stat52 + stat53 + stat54 + stat55 + stat56 + ## stat57 + stat58 + stat59 + stat60 + stat61 + stat62 + stat63 + ## stat64 + stat65 + stat66 + stat67 + stat68 + stat69 + stat70 + ## stat71 + stat72 + stat73 + stat74 + stat75 + stat76 + stat77 + ## stat78 + stat79 + stat80 + stat81 + stat82 + stat83 + stat84 + ## stat85 + stat86 + stat87 + stat88 + stat89 + stat90 + stat91 + ## stat92 + stat93 + stat94 + stat95 + stat96 + stat97 + stat98 + ## stat99 + stat100 + stat101 + stat102 + stat103 + stat104 + ## stat105 + stat106 + stat107 + stat108 + stat109 + stat110 + ## stat111 + stat112 + stat113 + stat114 + stat115 + stat116 + ## stat117 + stat118 + stat119 + stat120 + stat121 + stat122 + ## stat123 + stat124 + stat125 + stat126 + stat127 + stat128 + ## stat129 + stat130 + stat131 + stat132 + stat133 + stat134 + ## stat135 + stat136 + stat137 + stat138 + stat139 + stat140 + ## stat141 + stat142 + stat143 + stat144 + stat145 + stat146 + ## stat147 + stat148 + stat149 + stat150 + stat151 + stat152 + ## stat153 + stat154 + stat155 + stat156 + stat157 + stat158 + ## stat159 + stat160 + stat161 + stat162 + stat163 + stat164 + ## stat165 + stat166 + stat167 + stat168 + stat169 + stat170 + ## stat171 + stat172 + stat173 + stat174 + stat175 + stat176 + ## stat177 + stat178 + stat179 + stat180 + stat181 + stat182 + ## stat183 + stat184 + stat185 + stat186 + stat187 + stat188 + ## stat189 + stat190 + stat191 + stat192 + stat193 + stat194 + ## stat195 + stat196 + stat197 + stat198 + stat199 + stat200 + ## stat201 + stat202 + stat203 + stat204 + stat205 + stat206 + ## stat207 + stat208 + stat209 + stat210 + stat211 + stat212 + ## stat213 + stat214 + stat215 + stat216 + stat217 + x18.sqrt

## Slide 12: Full Model Analysis | Fit Statistics
Only a handful of predictors were statistically significant.
  This was expected based on the correlation of features to output analyzed in the exploratory analysis
  Variable selection may be appropriate here to remove unnecessary predictor variables
Adjusted
  Fairly low and expected based on low correlation of features to outputs
  Should two-way interactions be added to improve predictions?
    Increases predictors by
    Hence not practical
  In the future, we may need to do intelligent (selective) feature engineering using domain expertise to improve prediction capability.
    Outside the scope of this project.
## Estimate Std. Error t value Pr(>|t|) ## (Intercept) 1.969e+00 9.662e-03 203.750 < 2e-16 *** ## x4 -5.222e-05 9.162e-06 -5.700 1.26e-08 *** ## x7 1.100e-02 6.445e-04 17.067 < 2e-16 *** ## x8 4.087e-04 1.496e-04 2.732 0.006319 ** ## x9 3.277e-03 3.331e-04 9.837 < 2e-16 *** ## x10 1.133e-03 3.105e-04 3.649 0.000266 *** ## x11 1.913e+05 7.468e+04 2.562 0.010441 * ## x16 8.077e-04 2.156e-04 3.746 0.000181 *** ## x17 1.543e-03 3.305e-04 4.670 3.09e-06 *** ## x21 9.510e-05 4.254e-05 2.235 0.025438 * ## stat4 -5.043e-04 2.513e-04 -2.007 0.044807 * ## stat14 -8.553e-04 2.486e-04 -3.440 0.000587 *** ## stat22 -6.522e-04 2.506e-04 -2.603 0.009280 ** ## stat23 6.596e-04 2.481e-04 2.659 0.007864 ** ## stat24 -5.513e-04 2.502e-04 -2.203 0.027603 * ## stat26 -5.280e-04 2.497e-04 -2.114 0.034526 * ## stat33 -4.696e-04 2.495e-04 -1.883 0.059805 . ## stat35 -4.922e-04 2.503e-04 -1.967 0.049287 * ## stat54 -4.365e-04 2.520e-04 -1.732 0.083294 . ## stat59 4.344e-04 2.505e-04 1.734 0.083008 . ## stat60 5.615e-04 2.500e-04 2.247 0.024708 * ## stat65 -4.997e-04 2.510e-04 -1.991 0.046550 * ## stat92 -6.349e-04 2.504e-04 -2.536 0.011252 * ## stat98 3.533e-03 2.466e-04 14.323 < 2e-16 *** ## stat100 5.634e-04 2.509e-04 2.246 0.024743 * ## stat110 -3.305e-03 2.491e-04 -13.269 < 2e-16 *** ## stat146 -8.646e-04 2.517e-04 -3.435 0.000596 *** ## stat148 -4.893e-04 2.476e-04 -1.976 0.048161 * ## stat149 -4.674e-04 2.520e-04 -1.855 0.063657 . ## stat161 4.458e-04 2.511e-04 1.775 0.075936 . ## stat170 -4.629e-04 2.513e-04 -1.842 0.065485 . ## stat172 4.434e-04 2.478e-04 1.789 0.073601 . ## stat175 -4.131e-04 2.501e-04 -1.652 0.098633 . ## stat187 -4.999e-04 2.485e-04 -2.012 0.044304 * ## stat202 -4.297e-04 2.545e-04 -1.688 0.091467 . ## stat214 -4.480e-04 2.510e-04 -1.785 0.074341 . ## x18.sqrt 2.549e-02 9.552e-04 26.685 < 2e-16 *** ## --- ## Signif. codes: 0 '***' 0.001 '**' 0.01 '*' 0.05 '.' 0.1 ' ' 1 ## (Note: only showing the significant predictors above) ## Residual standard error: 0.03167 on 5343 degrees of freedom ## Multiple R-squared: 0.2607, Adjusted R-squared: 0.2275 ## F-statistic: 7.851 on 240 and 5343 DF, p-value: < 2.2e-16

## Slide 13: Full Model Analysis | Plots and Model Assumptions
Independence
  Since the features were sampled randomly, the independence assumption has been met.
Normality
  Histogram and QQ plot of residuals shows that they are not normally distributed
  Residual Plot shows that there are several values beyond the 2 sigma line again pointing to non-normality
  However, given the large sample size, this may not be much of a concern by itself
Equal Variance
  The residual plot shows that the points do not exhibit equal variance at all predicted levels.
  Points at the lower predicted levels have much smaller variance compared to other points
Notes: Am I missing an assumption here?

## Slide 14: Full Model Analysis | Case Influence Statistics
Cook’s D plot shows that there are several points beyond the 4/n line
  Not practical to analyze all points manually
  These points are influential and hence can impact the model coefficients adversely
It is tempting to remove them since, it improves the model fit drastically
  After consulting with domain experts, we found that these are valid points and hence there is no justification to remove them.
  Hence, we will proceed with these points included, noting that the assumptions for linear regression have not been satisfied entirely.
With High Cook’s D points removed
## [1] "Number of data points that have Cook's D > 4/n: 288"
Notes: Add color to the 4/n line and make thick

## Slide 15: Variable Selection Process
Try various variable selection techniques
  Forward Selection
  Backward Elimination
  Stepwise Selection
  LASSO
  LARS
Compare fit statistics and performance on test set
Pick best model

## Slide 16: Variable Selection Comparison
All techniques give essentially the same fit statistics.
Forward Selection, Backward Elimination and Stepwise Selection have only 13 predictors in the final model
LASSO and LARS have 37 predictors in the final model
Best Model: Backward Elimination (since it has the least predictors)
Algorithm | # Variables |  |  | RMSE (Train) | MAE (Train) | RMSE (Test)
Full Model | 240 |  |  |  |  | 
Forward Selection | 13 | 0.217 |  | 0.0319 | 0.0244 | 0.031
Backward Elimination | 13 | 0.218 |  | 0.0319 | 0.0244 | 0.031
Stepwise Selection | 13 | 0.218 |  | 0.0319 | 0.0244 | 0.031
LASSO | 37 | 0.217 |  | 0.0319 | 0.0245 | 0.031
LARS | 37 | 0.217 |  | 0.0319 | 0.0245 | 0.031
Algorithm | # Variables |  |  | RMSE (Train) | MAE (Train) | RMSE (Test)
Full Model | 240 |  |  |  |  | 
Forward Selection | 13 | 0.217 |  | 0.0319 | 0.0244 | 0.031
Backward Elimination | 13 | 0.218 |  | 0.0319 | 0.0244 | 0.031
Stepwise Selection | 13 | 0.218 |  | 0.0319 | 0.0244 | 0.031
LASSO | 37 | 0.217 |  | 0.0319 | 0.0245 | 0.031
LARS | 37 | 0.217 |  | 0.0319 | 0.0245 | 0.031
Notes: Changed MSE (Test) to RMSE (Test) for easier comparison, else the scales are vary different
Need to update code accordingly

## Slide 17: Best Model | Training Progression
RMSE was used to choose the final model during training
Lowest value of RMSE obtained for
Same for MAE and as well.

## Slide 18: Best Model | Variables, Coefficients, Confidence Intervals
Final model includes some of the same variables that we identified to be highly correlated to output in the exploratory analysis
## [1] "Coefficients of final model:" ## Estimate 2.5 % 97.5 % ## (Intercept) 1.997264e+00 1.990119e+00 2.004409e+00 ## x4 -5.208812e-05 -6.967037e-05 -3.450587e-05 ## x7 1.087549e-02 9.638690e-03 1.211229e-02 ## x8 4.449295e-04 1.574138e-04 7.324453e-04 ## x9 3.273601e-03 2.632944e-03 3.914258e-03 ## x10 1.057845e-03 4.603127e-04 1.655378e-03 ## x16 8.335013e-04 4.194785e-04 1.247524e-03 ## x17 1.504412e-03 8.703803e-04 2.138443e-03 ## stat14 -7.961817e-04 -1.272531e-03 -3.198326e-04 ## stat92 -7.279772e-04 -1.210233e-03 -2.457216e-04 ## stat98 3.613590e-03 3.139791e-03 4.087389e-03 ## stat110 -3.175507e-03 -3.655198e-03 -2.695815e-03 ## stat146 -8.450001e-04 -1.328278e-03 -3.617223e-04 ## x18.sqrt 2.528483e-02 2.345068e-02 2.711899e-02
variable | y3.log
x18 | 0.3120
x7 | 0.2091
stat98 | 0.1784
x9 | 0.1127
x17 | 0.0611
x16 | 0.0489
x10 | 0.0472
x21 | 0.0412
x11 | 0.0322
x8 | 0.0318
stat156 | 0.0287
stat23 | 0.0234
stat100 | 0.0206
stat144 | 0.0203
stat59 | 0.0202
stat60 | 0.0199
stat195 | 0.0199
stat141 | 0.0194
stat73 | 0.0192
stat197 | 0.0185
variable | y3.log
stat110 | -0.1594
x4 | -0.0603
stat13 | -0.0345
stat41 | -0.0345
stat14 | -0.0317
stat149 | -0.0309
stat113 | -0.0279
stat4 | -0.0248
stat106 | -0.0236
stat146 | -0.0236
stat186 | -0.0217
stat91 | -0.0210
stat214 | -0.0209
stat5 | -0.0207
stat22 | -0.0202
stat39 | -0.0202
stat175 | -0.0194
stat187 | -0.0193
stat128 | -0.0192
stat37 | -0.0191

## Slide 19: Best Model | Residual Analysis
Histogram of residual shows similar right skewed distribution as was seen in the full model.
Equality of variance at lower values of prediction is questionable as before.
Conclusion: Final model after variable selection suffers from same assumption violations as the full model.

## Slide 20: Best Model | Inference and Conclusion
Given the fact that the features were sampled randomly, any predictions drawn from this model can be applied to the entire design and manufacturing space of the integrated circuit.
Causality is not a concern here since the goal is mainly prediction of performance using the model.
However, given the fact that some of the model assumptions for multiple linear regression have not been met, we should be careful in using this model to predict new values

## Slide 21: Model Improvement Recommendations
Intelligent feature engineering to improve prediction performance.
Use non parametric models that do not need to satisfy normality and equal variance assumptions.
Divide data into clusters and model each cluster separately. (show box plot of high vs. low Cook’s D points).